## Slide 1: Project CANDL
Final Presentation
November 23, 2020

## Slide 2: Problem Statement
Current product: HEM Data OBD Logger
  Reads CAN bus
  Logs GPS data
  Stores info
  Uploads over 3G to remote server
Cost of current solution: over $800 per logger
Need a more cost-effective solution
New device should have upgrades over the current product

## Slide 3: Objectives
Accurately read and record CAN messages and sensor data from golf, utility, and consumer vehicles
Log location information via GPS
Upload captured data to a remote server via LTE or Wi-Fi
Process uploaded data and generate reports

## Slide 4: Deliverables
Printed Circuit Board (PCB) Files
Development Boards with Working Code Loaded
Schematics
Design Notes, Files
Testing Data
Code and Documentation
Notes: Ethan

## Slide 5: Design Sections
Hardware
  Power Supplies
  Microcontroller & CAN
  Wireless Communication Modules
Software
  Embedded
    RTOS & MQTT
    Wireless Configuration
    Data Collection
  Back-End
Notes: Ethan

## Slide 6: Hardware
Schematic and PCB Design

## Slide 7: System Architecture

## Slide 8: Power Supplies
Component supply requirements table
Four power domains: 3.3V, 3.8V, 1.8V, 5V
Three power supply ICs chosen

## Slide 9: Power Supplies
LTC3636​
  Dual-Channel SMPS​
  3.3V (Microcontroller, Wi-Fi Module, CAN Transceiver, Level Shifter)​
  3.8V (Cellular Module)​
  Up to 6A on each rail​
  12V input​
  $4.45 @ 1k units​

## Slide 10: Power Supplies
LT3080 (x2)​
  Single-Resistor LDO​
  5V and 1.8V​
  Up to 1.1A​
  12V input​
  $1.08 @ 1k units​
500µA on output required to operate correctly

## Slide 11: Microcontroller
STM32L443RC
  32-bit, ARM Cortex-M4, 80 MHz
  256KB Flash, 64KB SRAM
  1.71V – 3.6 V
  LQFP64 vs UFBGA64
    QFPs are suspectable to bent pins, easier to spot, and rework much easier.
Interfaces
  4 USART
  CAN
  USB 2.0
  3 SPI
  SDMMC
$2.85 @ 10k units

## Slide 12: Microcontroller Peripherals
SDIO: is an interface designed as an extension for the existing SD card standard
CAN: CANRX_TX for the CAN_H and CAN_L
USART: Universal Synchronous Asynchronous Receiver Transmitter
  UART: Universal Asynchronous Receiver Transmitter
  is a microcontroller peripheral that converts incoming and outgoing bytes of data into a serial bit stream

## Slide 13: CAN & CAN Transceiver
CAN: Controller Area Network
  allow microcontrollers and devices to communicate with each other's applications without a host computer
    Electronic equipment for aviation and navigation
    Car air-conditioning
CAN Transceiver: interface between a controller area network (CAN) protocol controller and the physical bus
    Receive Data for CAN
    $0.60 @ 1k units

## Slide 14: Microcontroller
Decoupling (4x 0.1uF , 1x10uF)
Reset Switch (Tactile Switch)

## Slide 15: Microcontroller Peripherals
SDIO: SD-Card
USART: LTE
UART: EC21
CAN: CAN - TX_RX
Level Shifters: 3.3V to 1.8V

## Slide 16: Wireless Modules
Cellular
Secondary means of communication
Wi-Fi
Primary means of communication

## Slide 17: Wireless Modules - Cellular
Quectel EC21-V
LTE Cat 1(10Mbps down, 5 Mbps up)
GNSS included
UART or USB interface

## Slide 18: Wireless Modules – Cellular

## Slide 19: Wireless Modules – Wi-Fi
Quectel FC20
Compatible with EC21-V
Dual-band Wi-Fi
BT v4.2
Interfaces directly to EC21-V via SDIO
UART for BT functionality

## Slide 20: Wireless Modules – Wi-Fi

## Slide 21: Printed Circuit Board
Four-layer design
  Top Layer: Signal 1
  Layer 2: Ground
  Layer 3: Split power – 1.8V and 3.3V
  Bottom Layer: Signal 2
Two boards created
  Complete Board: includes all components
  Test Board: excludes RF components (LTE, Wi-Fi) and adds headers for testing connections to cellular development kits
Future improvements: shields, more layers, ground pours and traces, RF noise reduction

## Slide 24: Embedded Software
RTOS, Wireless Communications, Data Collection

## Slide 25: RTOS
RTOS – Real Time Operating System
  Manages memory and threads
  Used in embedded systems because it uses a small amount of resources
  We are using Amazon’s FreeRTOS
    Good documentation
    Widely used and supported
  Two threads
    Store CAN data
    Send data to the server

## Slide 27: MQTT
Messaging protocol for IOT systems
Chosen because
  Popular and simple
  Team already familiar with it
Topics: UID/<topic name>
  CAN
  GPS
  Command
  Error
Message Format
  { “msg_id”: “<CAN id #>”, “payload”: “<CAN data>”, “timestamp”: “<time>”}

## Slide 28: Wireless Configuration
Wireless modules are configured by AT commands.
Uses Interrupt for receive due to variable length nature of Response codes.
Wi-Fi pushed for future goals due to issues getting UART setup.
GPS data is to be received over second UART port ‘UART3’. Additional information from GPS includes time and date, location, and speed information.
Potential Future used for FC-20 (not N version), Bluetooth for future sensors.

## Slide 29: Data Collection
Goals:
Interrupt-driven reception from CAN Bus
Save data to microSD
Process:
Initialize CAN in MX_CAN_Init
Overwrite receive interrupt callback function
Start data collection
Create FAT file system
Write data to text file
Future improvements: Loopback reception and filters

## Slide 30: Back-End Software
Server Scripts, Data Analytics

## Slide 31: Server-Side Software
Objective: Data decoding and Data Storage
MQTT Broker
  Mosquitto broker service
  SUB/PUB model
MySQL Server
  Candl_data database
  Tables by CAN message ID
  Store historical CAN data

## Slide 32: Server-Side Software
Python Scripts
  MQTT Listener Client
    Subscribed to all MQTT topics
    On message receive, decode the message payload
    Pass decoded payload to SQL insertion functions
  Database Manager
    Establish connection to SQL database
    Format data into SQL query
    Use query to insert data into tables

## Slide 33: Project Management
Bill of Materials, Budget

## Slide 34: Bill of Materials
Target price: $50
Actual price: $42.38

## Slide 35: Budget
Total project budget: $1500.00
Total development cost: $903.94

## Slide 36: Questions?
live DEMO